# Text boxes

Decrease cell coverage area

YES

Estimate Interference level

Monitor Traffic Measurement Reports at MSC

Identify cell coverage areas

Existing System

Determine anticipated load 
per sector (Erlangs) for the existing cells coverage area.

Traffic Engineering Decision Flowchart

YES

NO

NO

YES

NO

Is GOS ( desired % (2-5%)

Is # channels/cell < Available Cell Capacity?

Is interference requirement satisfied?

END

New System

Obtain service area maps

Obtain demographics (population)

Obtain vehicular traffic intensity

Determine subscriber numbers

Specify cell site type (Omnidirectional or Sectored)

Specify GOS (2-5% of blocking)

Specify capacity for growth (25%)

Decrease cell coverage area

END

Sectorize site (if omni) to 3-sector , add more capacity to the area by frequency plan changes, 
or accept a lower GOS

Determine number of channels per cell

Determine anticipated load 
per new cell or sector (Erlangs)

Determine average load per subscriber (Erlangs)